Universal Serial Bus 3.0

---
Introduction
- Released in November 2008
- 10 times faster than USB 2.0

---
Features
- Speed : 5 Gigabits/second
- Full duplex data transfer
- Backward USB 2.0 compaitable
- Maximum current : 900 mA
- No polling and broadcasting

---
USB 3.0 Cable

---
Speed Comparison

---
USB 3.0 Architecture

---
Difference between USB 2.0 & 3.0

---
SuperSpeed Device Detection

---
Device Enumeration
- Rx detect tells if the device is Super speed
- Device gets reset
- Device will be in default state and draws power no more tha 150 mA
- Host assigns unique address to device
- Reads descriptor to find the maximum payload size and to learn about the device
- Loads the specific driver to start commmunication

---
Layers in USB 3.0
- Physical Layer
- Link Layer
- Protocol Layer

---
Link Layer
- Error Checking using CRC
- Sequence Numbering
- Packets Framing
- Link commands (verify successful transmission)
- Ordered sets for synchronization

---
Protocol Layer
- End to end communication
- Defines set of rules for communication

---
Packets
- Transaction packet
- Data packet
- Link management packet
- Isochronous time stamp packet

---
Transaction packet

---
Data Packet

---
Link Management packet

---
Isochronous Timestamp packet

---
IN Transaction protocol

---
Out Transaction protocol

---
Transfer types
- Control transfer
- Bulk transfer
- Interrupt transfer
- Isochronous transfer

---
Control transfer
- Host uses control transfer to get information about the device
- 20 percentage of banwidth is allocated to control transfer
- Maximum data packet size : 512 bytes

---
Bulk transfer
- Bulk transfer is used to transmit large amount of data
- Bulk transfer uses 20 percentage of bus bandwidth
- Maximum data packet size : 1024 bytes

---
Interrupt transfer
- Interrupt transfer are used to get the status update from a device
- Interrupt and isochronous transfer can combinely use 90 percentage of bandwidth
- Maximum data packet size : 1024 bytes

---
Isochronous transfer
- Isochronous transfer are used in transferring real time data
- Interrupt and isochronous transfer can combinely use 90 percentage of bandwidth
- Maximum data packet size : 1024 bytes

---
USB descriptors
- Device descriptor
- Configuration descriptor
- Interface descriptor
- Endpoint descriptor
- BOS descriptor
- Capability descriptor